Computer Networks

Assignment 5
Group 12

Ishan Arif Mardani (21CS01023)
Vishnu Tirth Bysani (21CS01077)
Akshit Dudeja (21CS01026)

Q1

In order to execute the TCL script, do the following:
1. Ensure that NS2 and NAM are installed on your PC and run the script in the directory of the file.
2. Use the following command to execute: ns Q1.tcl

Output -

Unreliable connection between C to D.

Reliable connection between D to B.

FTP connection between A to B via D.

The parameters regarding the following program are:
1. From C->D : Duplex Link, Data Rate: 10 Mb, Time: 2 ms
2. From B->D : Duplex Link, Data Rate: 10 Mb, Time: 2 ms
3. From A->D : Duplex Link, Data Rate: 10 Mb, Time: 2 ms
Also, between C and D, an unreliable connection is present. We have taken traffic type of UDP along with CBR. C is the source and D is the sink.
Also, between D and B, a reliable connection is present. We have taken the traffic type of TCP along with FTP. D is the source and B is the sink.
Also, between A and B (via D), we have taken the traffic type of TCP along with FTP. A is the source and B is the sink.
End-to-end Delay Calculation:
Average end-to-end delay for node 0 is 0.0
Average end-to-end delay for node 1 is 0.005725180671649381
Average end-to-end delay for node 2 is 0.0
Average end-to-end delay for node 3 is 0.004581611527782843
Conclusion:
There is no delay in node 0 and node 2 as they are the sending packets. The code has been attached below for reference. A library called traceanalyzer has been used for the calculation of delay time.

import traceanalyzer as tr / #end-to-end delay / eedelay0=tr.Eedelay('Q1/first.tr','0') eedelay1=tr.Eedelay('Q1/first.tr','1') eedelay2=tr.Eedelay('Q1/first.tr','2') eedelay3=tr.Eedelay('Q1/first.tr','3') / #Calculate the averages arr0 = eedelay0.eedelay_array arr1 = eedelay1.eedelay_array arr2 = eedelay2.eedelay_array arr3 = eedelay3.eedelay_array / print("Average end-to-end delay for node 0 is " , sum (arr0) / len (arr0)) print("Average end-to-end delay for node 1 is " , sum (arr1) / len (arr1)) print("Average end-to-end delay for node 2 is " , sum (arr2) / len (arr2)) print("Average end-to-end delay for node 3 is " , sum (arr3) / len (arr3))

Q2

In order to execute the TCL script, do the following:
1. Ensure that NS2 and NAM are installed on your PC and run the script in the directory of the file.
2. Use the following command to execute: ns Q2.tcl

Output -

Unreliable connection between C to B.

FTP connection between A to B.

Reliable connection between B to D.

The parameters regarding the following program are:
1. From C->B : Duplex Link, Data Rate: 10 Mb, Time: 2 ms
2. From A->B : Duplex Link, Data Rate: 10 Mb, Time: 2 ms
3. From B->D : Duplex Link, Data Rate: 10 Mb, Time: 2 ms
Also, between C and B, an unreliable connection is present. We have taken traffic type of UDP along with CBR. C is the source and D is the sink.
Also, between A and B, a reliable connection is present. We have taken the traffic type of TCP along with FTP. D is the source and B is the sink.
Also, between B and D (via D), we have taken the traffic type of TCP along with FTP. A is the source and B is the sink.
End-to-end Delay Calculation:
Average end-to-end delay for node 0 is 0.0
Average end-to-end delay for node 1 is 0.004932347886719936
Average end-to-end delay for node 2 is 0.0
Average end-to-end delay for node 3 is 0.013755222454672013

Conclusion:
There is no delay in node 0 and node 2 as they are the sending packets. The code has been attached below for reference. A library called traceanalyzer has been used for the calculation of delay time.

import traceanalyzer as tr / eedelay0=tr.Eedelay('Q2/second.tr','0') / eedelay1=tr.Eedelay('Q2/second.tr','1') / eedelay2=tr.Eedelay('Q2/second.tr','2') / eedelay3=tr.Eedelay('Q2/second.tr','3') / arr0 = eedelay0.eedelay_array / arr1 = eedelay1.eedelay_array / arr2 = eedelay2.eedelay_array / arr3 = eedelay3.eedelay_array / print("\nFor Q2") / print("Average end-to-end delay for node 0 is " , sum (arr0) / len (arr0)) / print("Average end-to-end delay for node 1 is " , sum (arr1) / len (arr1)) / print("Average end-to-end delay for node 2 is " , sum (arr2) / len (arr2)) / print("Average end-to-end delay for node 3 is " , sum (arr3) / len (arr3))